|  |  |  | Engine Model |  | Curve No. |  | DCEC |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | Dongfeng Cummins Engine Company |  | 6BTA5.9-C170 |  | FR91342 |  |  |
|  | Xiangyang - Hubei, China |  |  |  |  |  |  |
|  |  |  | Engine Family |  | CPL Code |  | Date |
|  | Construction Engine Data Sheet |  | D40 |  | 8541 |  | 2006-06 |
| Displacement: 5.9L | Advertised Power: 125kW@2300 rpm |  |
| Bore: 102mm |  |  | 170HP@2300 rpm |  |
| Stroke: 120mm | Peak Torque: | 630N.m@1400 rpm |  |
| Fuel System: Weifu AD Pump/RSV | Aspiration: Turbocharged &water air cooled |
| Cylinders: 6 Cylinders, in Line | Rating Type: Continuous |  |

Emission Control:

Engine in testing with fuel system, water pump, oil pump, with no air compressors, alternators, fan, optional items. Test conditions for 250 mm water column inlet resistance, exhaust resistance 50 mm hg

Power Curve of Cummins 6BTA5.9-C170 Diesel Engine

All performance data based on the standard status and GB/T18297 conditions.

Cummins 6BTA5.9-C170	www.enginecummins.com

Cummins Engine Co. Ltd

Diesel Engine for Construction Performance Data

General Engine Data

Engine Wet Weight (Pricing Configuration)…………………………………………………………………. 443 kg

Moment of Inertia of Rotating Components (No Flywheel)……………………………………..………… 0.25 kg·m2

Center of Gravity from Front Face of Block…………………………………………………………..……... 391 mm

Center of Gravity above Crankshaft Centerline……………………………………………………….……… 140 mm

Crankshaft Thrust Bearing Load Limit

—Maximum Intermittent………………………………………………………………………. 3425 N

—Maximum Continuous……………………………………………………………………….. 1112 N

Engine Mounting

Maximum (Static) Bending Moment at Front Support Mounting Surface…………………………………… 435 N.m

Maximum (Static) Bending Moment at Side Pad Mounting Surface………………………………………… TBD N.m

Maximum (Static) Bending Moment at Rear Face of Block…………………………………………………. 1356 N.m

Moment of Inertia of Complete Engine

— Roll Axis………………………………………………………………………………….… 16.5 kg·m2

— Pitch Axis…………………………………………………………………………………… 41.1 kg·m2

— Yaw Axis……………………………………………………………………………………. 35.4kg·m2

Exhaust System

Maximum Back Pressure…………………………………………………………………………………….. 76 mmHg

Exhaust Pipe Size Normally Acceptable……………………………………………………………………...	75 mm

Maximum Static Supported Weight at the Turbocharger Outlet Flange……………………………………... 13.5 N·m

Exhaust Manifold Insulation Acceptable………………………………………………………………….…..	N/A

Turbocharger Insulation Acceptable………………………………………………………………………….	N/A

Air Intake System

Maximum Intake Air Restriction with Heavy Duty Air Cleaner

— Clean Element……….…………………………….………………………………………….. 381 mmH2O

— Dirty Element……….…………………………………….…………………………………... 635 mmH2O

Minimum Dirt Holding Capacity with Heavy Duty Air Cleaner……………………………………………. 53 g/litre/sec.

Maximum Temperature Rise from Ambient to the Inlet of the Turbocharger……………………………….	17 ℃

Maximum Pressure Drop from the Turbocharger Outlet to the Intake Manifold…………………………….	TBD kPa

Lubrication System

Normal Operating Oil Pressure Range…….………………………………………………………………… 69 – 345 kPa

Maximum Lube Oil Flow for Engine Accessories…….…………………………………………………….. 4.0 litre/min.

Maximum Sump Oil Temperature……………….…………………………………………………………..	127 ℃

Minimum Engine Oil Pressure for Engine Protection Devices:

Cummins 6BTA5.9-C170	www.enginecummins.com

— At Rated Speed and Load………………………………………………………………..…......	276 kPa

— At Torque Peak Speed and Load………………………………………………………..…...….   207 kPa

— At Low Idle…………………………………………………………………………….……….69 kPa

Minimum Required Lube System Capacity - Sump plus Filters…….……………………………..………	16.3 litre

| By-pass Filtration Required………………………………………………….……………………………… | No |
| --- | --- |
| Angularity of Standard Oil Pan: (Values stated are for intermittent operation only): |  |
| — Front Down…………………………………………………………………………………….. | 45 º |
| — Front Up………………………………………………………………………………………… | 45º |
| — Side to Side……………………………………………………………………………………... | 45º |
| Cooling System |  |
| Coolant Capacity - Engine Only…………………………………………………………………………….. | 10.4 L |
| Maximum Engine Cooling Circuit External Resistance……………………………………………………... | 34 kPa |
| Minimum Pump Inlet Pressure with Open Thermostat and no Pressure Cap……………………………….. | TBD |
| Maximum Static Head of Coolant Above Engine Crankshaft Centerline…………………………………… | TBD |
| Standard (modulating) Thermostat Range…………………………………………………………………… | 82-93 ℃ |
| Maximum Block Coolant Pressure with Closed Thermostat and no Pressure Cap…………………………. | 276 kPa |
| Minimum Pressure Cap……………………………………………………………………………………… | 50 kPa |
| Maximum Engine Coolant Temperature at Engine Outlet………………………………………………….. | 100℃ |
| Maximum Engine Coolant Temperature for Engine Protection Devices……………………………………. | 101.6℃ |
| Minimum Engine Coolant Temperature……………………………………………………………………... | 71℃ |
| Minimum Fill Rate…………………………………………………………………………………………… | 19 litre/min |
| Maximum Initial Fill Time…………………………………………………………………………………… | 5 min |
| Minimum Coolant Expansion Space………...………….………….………………………………….6% of System Capacity |
| Maximum Deaeration Time…………………………………………………………………………………. | 25 min. |
| Minimum Drawdown………………………………….……………………………….………11% of Total System Capacity |
| (Drawdown Must Exceed the Volume Not Filled at Initial Fill & Must Not Include Expansion Space) |  |
| Fan-on Engine Coolant Outlet Temperature………………………………………………………………… | 93℃ |
| Shutter Opening Coolant Outlet Temperature……………………………………………………………….. | 85℃ |
| Shutter Opening Intake Manifold Air Temperature…………………………………………………………. | 65.6 |
| Fueling System |  |
| Maximum Fuel Flow on the Supply Side of the Fuel Pump……………………………………………….. | 193 kg/hr |

— with clean fuel filter………………………………………………………………………..   102 mmHg

— with dirty fuel filter………………………………………………………. ………………. 203 mmHg Maximum Fuel Drain Restriction

— with check valves…………………………………………………………………………..TBD

— less check valves…………………………………………………………………………...   510mmHg

| Maximum Fuel Inlet Temperature…………………………………………………………………………. | 71℃ |
| --- | --- |
| Minimum Fuel Tank Air Venting Capability Required at 6 in. H2O Back Pressure……………………… | 340 litre/hr |
| Low Idle Set Speed………………………………………………………………………………………… | 750 rpm |

Cummins 6BTA5.9-C170	www.enginecummins.com

| Maximum Governed Speed（10% of Rated Torque）.…………………………………………………… | 2450 rpm |
| --- | --- |
| Maximum Over speed Capability………………………………………………………………………….. | 3750 rpm |
| Emission |  |  |  |  |  |  |  |  |  |  |  |
| Estimated Free Field Sound Pressure Level At 15 m (50 ft.) and Full-Load Governed Speed |  |  |  |
| (Excludes Noise from Intake, Exhaust, Cooling System and Driven Components) |  |  |  |  |  |  |  |  |
|  | —Right Side…………………………………………………………………………………... | N/A |
|  | —Left Side…………………………………………………….………………………………. | N/A |
|  | ...—Front……………………………………….……………………………………………… |
|  | .. ..—Rear………………………………………………………………………………………. |
|  |  |  |  | Rated |  |  | Max. |  |  | Peak |  |  |
|  | Fuel Rating Option used for these Data: FR91342 |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  | Power |  |  | Power Point |  |  | Torque |  |  |
|  | Engine Speed…………………………………….… -rpm |  | 2300 |  |  |  |  |  | 1400 |  |  |
|  | Gross Power Output…………………..…………… -kW |  | 125 |  |  |  |  |  | 92.4 |  |  |
|  | Torque……………………………………………... -N.m |  | 518 |  |  |  |  |  | 630 |  |  |
|  | Intake Manifold Pressure……………………...…… -kPa |  | 100 |  |  |  |  |  | 75 |  |  |
|  | Motoring Friction Horsepower…………………..… -kW |  | 20 |  |  |  |  |  | 9 |  |  |
|  | Turbocharger Compressor Outlet Pressure..….……. -kPa |  | 105 |  |  |  |  |  | 75 |  |  |
|  | Intake Air Flow………………………………..…… -litre/sec |  | 217 |  |  |  |  |  | 111 |  |  |
|  | Exhaust Gas Flow………………….………….…… -litre/sec |  | 500 |  |  |  |  |  | 245 |  |  |
|  | Exhaust Gas Temperature - Dry Stack…….……..… -℃ |  | 450 |  |  |  |  |  | 530 |  |  |
|  | Heat Rejection to Ambient (Dry Manifol………..… -kW |  | TBD |  |  |  |  |  | TBD |  |  |
|  | Heat Rejection to Coolant (Dry Manifold)………… -kW |  | 80 |  |  |  |  |  | 50 |  |  |
|  | Heat Rejection to Fuel……………………...……… -kW |  | 0.7 |  |  |  |  |  | 0.3 |  |  |
|  | Engine Coolant Flow…………….………………… -litre/sec |  | 3.2 |  |  |  |  |  | 2.0 |  |  |
|  | External Cooling Circuit Resistanc………………… - Kpa△P |  | 20.7 |  |  |  |  |  | 20.7 |  |  |
|  | Altitude Limitations: |  |  | N/A |  |  |  |  |  | N/A |  |
|  | —Intermittent…………………………………. | -m | 3050 |  |  |  |  |  | 3050 |  |  |
|  | —Continuous……………………….………….-m |  | TBD |  |  |  |  |  | TBD |  |
|  | Steady State Smoke…………….……………… | -Bosch | 1.5 |  |  |  |  |  | 2.5 |  |  |

ALL DATA CERTIFIED WITHIN 5%

TBD = To Be Decided N/A = Not Applicable N.A. = Not Available

All data is subject to change without notice, sorry for inform.

Cummins 6BTA5.9-C170	www.enginecummins.com